Revised Total Coliform Rule: Sample Siting Plan

System Name: _____________________________________ PWSID: MT_______________

Contact Name: ______________________________ Phone Number: __________________

- Routine and Repeat Sample Locations

| Routine Sample Sites Location/Address | Repeat Sample Sites Location/Address |
| --- | --- |
| X1. |  | 1-1. |
|  |  |  | 1-2. |
|  |  |  | 1-3. |
|  |  |  | Alternate site location: |
| X2. |  | 2-1. |
|  |  |  | 2-2. |
|  |  |  | 2-3. |
|  |  |  | Alternate site location |
| X3. |  | 3-1. |
|  |  |  | 3-2. |
|  |  |  | 3-3. |
|  |  |  | Alternate site location |
| X4. |  | 4-1. |
|  |  |  | 4-2. |
|  |  |  | 4-3. |
|  |  |  | Alternate site location |
| X5. |  | 5-1. |
|  |  |  | 5-2. |
|  |  |  | 5-3. |
|  |  |  | Alternate site location |

If the number of Routine samples needed to cover the distribution system requires more than five Routine sites, attach additional sheets as needed.

Routine Sample Rotation Schedule

| Month | Routine Site(s) | Month | Routine Site(s) |
| --- | --- | --- | --- |
| January |  | July |  |
| February |  | August |  |
| March |  | September |  |
| April |  | October |  |
| May |  | November |  |
| June |  | December |  |

- System Map

  - Please attach a map of this public water supply that identifies water system facilities (sources, storage, treatment, distribution and pressure zones) and sample point locations.

- Guidelines for Sample Site Selection

| Minimum Routine Sample Sites |
| --- |
| Service Connections | Samples Sites |
| 1 | 1 |
| 2 to 10 | 2 |
| 11 to 100 | 3 |
| 101 to 500 | 4 |
| 501 ≤ | 5 |

- Plumbing should be inspected to ensure no cross-connection with non-potable water sources exist

- The sampling tap should be free of any aerators, strainers, hoses or water treatment devices

- Leaking taps that allow water to flow over the outside of the tap should be avoided

- Outside taps, swivel taps and combined hot and cold water faucets should be avoided.

- Routine sample sites should be accessible daily and throughout the entire year

- No routine sample site should be the last service connection from any dead end of the water distribution system

- Select repeat sample site locations that would help you isolate the problem if one should occur. Repeat sample sites no longer have to be located within five service connections both upstream and downstream of each routine sample site

- Small systems may, if necessary, collect repeat samples at one or more of the other routine sample sites if they are located within five service connections of the original coliform-positive routine sample site

Please return to:		DEQ Public Water Supply Program

ATTN: RTCR Rule Manager

PO Box 200901, Helena, MT 59620-09901

Or email to DEQRTCRLEVEL12@mt.gov