## Slide 1: Establishing Nonanthropogenic Arsenic Standards for the Yellowstone River that Best Protect Human Health
Michael Suplee, Ph.D.
Water Quality standards & Modeling section
Montana Department of Environmental Quality
January 10, 2020
Water Pollution Control Advisory Council meeting

## Slide 2
Notes: Point out that we are addressing the upper and middle river, the transition between the two is around the Clarks Fork of the Yellowstone River. The five segments will be discussed later in the presentation. If anyone asks - each segment ends immediately upstream of the major tributary dividing it from the downstream segment.

## Slide 3: Background
DEQ developed nonanthropogenic arsenic criteria for parts of the Yellowstone River
  DEQ emphasized that—at these concentration ranges—the drinking water beneficial use is the use most likely to be effected.
  Concerns from industry resulted in WPCAC tabling the rulemaking (until 1/10/2020)
    Since then, additional analyses have been completed which modify DEQ’s recommendations as to how the standards should be expressed

## Slide 4: State Statutes Involved
75-5-222 (1): For parameters for which the standards are more stringent than the nonanthropogenic condition, the standard is the nonanthropogenic condition.
75-5-301(2): The board shall formulate and adopt WQ standards, giving consideration to the economics of waste treatment and prevention.
75-5-101: The state’s public policy is to conserve water by protecting, maintaining, and improving the quality and potability of water for public water supplies, wildlife, fish…

## Slide 5: An Objective Way to Assess the Best Expression of the Standards
Line of Reasoning: If adopting nonanthropogenic arsenic standards in a particular way—while conforming with the statutes—can demonstrably decrease cancer risk for people using the Yellowstone River as a water supply, then that is the best expression of the standards.

## Slide 6: Since the November 2019 WPCAC Meeting
Explored effects on the drinking water beneficial use when nonanthropogenic standards are expressed in different ways
  High Flow and Low Flow Seasonal Median Standards (2 values); vs.
  Single Annual Median Standard (1 value).
Question: Which nonanthropogenic standards (2 Seasonal, or 1 Annual) result in lower cancer risk to people drinking water from the Yellowstone River downstream from permitted arsenic discharges?
Must assume—or demonstrate—that arsenic in finished drinking water varies with river arsenic concentrations

## Slide 7: Arsenic in Billings finished drinking water varies with river arsenic concentration
Similar findings elsewhere:
Wilson et al., 2002. Arsenic removal in water treatment
facilities: Survey of geochemical factors and pilot plant
experiments. Illinois Waste Management & Research Center.

## Slide 8: Other Principles and Assumptions
Human cancer risk from a carcinogen like arsenic is continuous from origin (no safe lower conc.)
  Maximum Contaminant Level Goal (MCLG) = zero
  Arsenic is category A (known human carcinogen)
Cancer risk computed using accepted EPA equations
and risk factors, and assumptions adopted in DEQ-7:
Arsenic vs. cancer risk based on current EPA methods and assumptions In DEQ-7
(MCL: 10 µg/L = 7.37 X10-4 risk)
(equals <1 excess case in 1000)
EPA Health Advisory,
2018

## Slide 9: Methods
1. To meet 75-5-222, I asked “In each segment, does the
annual median ever occur during high flow?”
  Yes. Each annual median is within its corresponding nonanthropogenic high-flow conc. range
    Annual medians are within the “nonanthropogenic condition”
    Segment 4 example: Annual median = 13.0 µg/L, High FlowMAX = 13.7 µg/L
2. Computed new concentrations for each expression of the nonanthropogenic standards: A. River + discharge @ two seasonal standards, B. River + discharge @ one annual standard
  Long-term river flows computed as harmonic means (EPA, 1991)
3. Calculated total cancer risk associated with river concentrations resulting from bullet 2
Cnew = [(C1V1) + (C2V2)]÷(V1+V2)
River Discharge

## Slide 10: Summary of Findings

## Slide 11: Why do the Annual Standards Better Reduce Cancer Risk?
Example: Segment 1 (MT/WY Border to Mill Creek)
Greater dilution when it matters most…
Low Flow Stnd (µg/L)

## Slide 12: In Segment 1, cancer risk from the nonanthropogenic standards goes down incrementally as the standards are set to longer and longer timescales (monthly to seasonal, seasonal to annual)
Monthly Standards:
2.03525 X 10-3
Risk
2 Seasonal Standards:
2.03511 X 10-3
1 Annual Standard:
2.03494 X 10-3
In Segment 4, the pattern is not as consistent across the timescales, but the annual standard still has the lowest cancer risk.

## Slide 13: Other Findings
Permitted discharge volumes would have to be far in excess of the Yellowstone River’s highest flows to change the conclusions
Indicates that this approach must be very carefully evaluated where effluent dominated waterbodies are concerned

## Slide 14: Conclusions
Increases and decreases in the Yellowstone River’s arsenic concentrations are reflected in drinking water supplies that use the river
Therefore: an annual nonanthropogenic median is the better expression of the nonanthropogenic standard compared to two seasonal median standards
  Reduces cancer risk in segments 1-4
    Cancer risk reductions are small, on the order of 1/10,000,000 to 1/100,000,000
  Risk in segment 5 is the same via either approach
  Risk in segment 5 is apparently the same under DEQ-7

## Slide 15: Conclusions
Adopting the standards as annual nonanthropogenic medians meets the key statutes (Montana Code Annotated):
  Per 75-5-222(1): All annual medians are of lower concentration than the corresponding max nonanthropogenic high-flow values
    This means the annual medians are always within the “nonanthropogenic condition”
  Per 75-5-301(2): Annual median standards are apparently more economical
  Per 75-5-101: Annual median standards improve the quality and potability of water for public water supplies

## Slide 16: Future Monitoring and Assessment of Yellowstone River Arsenic
Wilson Interval was recommended for the two seasonal standards
Wilson Interval can also be used to evaluate annual median standards
  Proportional sampling of Low Flow (75%) and High Flow (25%) periods
  To detect <25% change in river’s median arsenic, with <10% false positives:
    N=16 samples per segment, collected over 1 year
      Zero exceedance=full compliance
      One exceedance= non compliance

## Slide 17: Recommended Standards
River Segment | Yellowstone River Segment Description | Annual Nonanthropogenic Arsenic Standard (µg/L)
1 | MT/WY Border to Mill Creek | 28
2 | Mill Creek to Boulder River | 22
3 | Boulder River to Stillwater River | 16
4 | Stillwater River to Clarks Fork of the Yellowstone | 13
5 | Clarks Fork of the Yellowstone to Bighorn River | n/a*
*In this segment the nonanthropogenic condition is not less that the standard so DEQ-7 standard would continue to apply. |  | 
OTHER ASPECTS OF THE NON-
ANTHROPOGENIC STANDARDS:
No use changes along the
Yellowstone River are proposed
Standards apply end-of-pipe; no
mixing zones
For permits, an average monthly
limit and a maximum daily limit
will be calculated per EPA
(1991) methods; “no sample shall
exceed” does not apply
Long-term ambient assessment
will evaluate changes in river’s
median arsenic concentration

## Slide 18: Discussion, Next Steps